## Slide 1
BESS Trading Strategies & The Role of Price Forecasting
How forecasting transforms battery storage from a scheduled asset into a trading machine
March 2026

## Slide 2
BESS Revenue Streams
⚡ Energy Arbitrage
Buy low, sell high on spot markets
Primary revenue driver Directly forecast-dependent
🔄 Frequency Regulation
FCR, aFRR — grid stabilization
Contracted availability Low forecast dependency
📊 Capacity Markets
Availability premiums for peak demand
Long-term contracts Minimal forecast need
📉 Peak Shaving
Reduce demand charges
Behind-the-meter Partial forecast benefit
⚖️ Balancing Mechanism
Real-time grid balancing
High-value, unpredictable Forecasting creates edge
💡 Arbitrage + Balancing = highest forecasting sensitivity → biggest revenue uplift from better predictions

## Slide 3
Day-Ahead: Known Prices ≠ Full Picture
✅ What You Know (12–36h ahead)
DA auction results published ~12:42 CET for next day
All 24 hourly prices are fixed and known
Optimal charge/discharge schedule can be computed via LP
No forecasting needed for pure DA execution
→ Simple: solve LP against known prices, execute schedule
❌ What You Don't Know
Intraday continuous prices (can deviate ±50% from DA)
Imbalance / settlement prices (can spike to 1,000+ €/MWh)
Tomorrow's DA prices (needed for multi-day planning)
Whether to reserve capacity for higher-value markets
Battery degradation trade-off: cycle today or save for tomorrow?
→ This is where forecasting creates real value

## Slide 4
Five Ways Forecasting Drives Revenue
1
Capacity Allocation
How much battery to commit to DA vs. reserve for intraday/balancing?
Forecast intraday volatility & balancing prices
2
Intraday Trading
Capture spreads between DA and intraday prices
Forecast 15-min intraday prices up to delivery
3
Multi-Day Planning
Skip weak spreads today, cycle on high-spread days
Forecast DA prices beyond known window
4
Imbalance Optimization
Position for settlement price spikes
Forecast system imbalance & balancing activation
5
Negative Prices
Get paid to charge during renewable oversupply
Forecast wind/solar surplus & demand troughs

## Slide 5
Forecast Horizons & Methods
Strategic
Long-Term 1–10 Years
Application
Investment decision, site selection, PPA pricing
Method
Fundamental models, Merit-Order simulation
Tactical
Medium-Term Weeks–Months
Application
Hedging, maintenance planning, seasonal strategy
Method
Weather ensembles + statistical models
Operational
Day-Ahead 12–36 Hours
Application
Dispatch optimization, auction bidding strategy
Method
ML models (LSTM, Transformer, XGBoost)
Trading
Intraday 0–4 Hours
Application
Continuous trading, position adjustment
Method
Real-time ML, order book analysis

## Slide 6
Revenue Impact: With vs. Without Forecasting
📋 Without Forecasting (DA-Only)
Fixed schedule based on known DA prices
1 cycle per day, no intraday trading
No multi-day optimization
Captures ~50–60% of available revenue
Misses intraday spikes & negative price events
Typical: €80–120k / MW / year
🚀 With Advanced Forecasting
Dynamic dispatch across DA + intraday + balancing
Multi-cycle on volatile days (2–3 cycles)
Degradation-aware multi-day planning
Captures ~80–95% of available revenue
Exploits negative prices & imbalance spikes
Typical: €120–180k / MW / year (+40–60%)
For a 100 MW BESS: forecasting can add €2–5M in annual revenue

## Slide 7
Price Curves: DA vs. Intraday vs. Imbalance — 36h View
Illustrative prices · DA = Day-Ahead (known) · Intraday & Imbalance = forecast-dependent · Spreads compound with multi-cycle and spike capture

## Slide 8
Next Frontier: Reinforcement Learning
Traditional: Forecast → Optimize → Execute
Market Data
→
Price Forecast
→
LP/MPC Optimizer
→
Dispatch Schedule
⚠️ Errors at each stage compound — forecast miss → suboptimal dispatch
RL: Market Signals → Optimal Action (End-to-End)
Market Signals
→
RL Agent (PPO/SAC)
→
Optimal Action
✅ No forecast error propagation — learns patterns implicitly
+5–15% vs. traditional forecast + optimize
Best in volatile & intraday markets
Production-ready: Habitat, Tesla, Enspired

## Slide 9
Key Takeaways
DA prices are known — but they're only the floor, not the ceiling
Pure DA execution captures ~50–60% of available revenue. The rest sits in intraday, imbalance, and cross-market optimization.
Forecasting unlocks 5 additional revenue levers
Capacity allocation, intraday trading, multi-day planning, imbalance optimization, and negative price exploitation.
Forecast accuracy directly impacts IRR
±5 vs. ±15 €/MWh forecast error can shift project IRR by 3–5 percentage points. For a 100 MW BESS: €2–5M annual difference.
RL is the next evolution — collapsing forecast + optimization
End-to-end learning eliminates forecast error propagation. +5–15% revenue vs. traditional approaches. Already deployed commercially.
The competitive moat in BESS is software, not hardware
Battery hardware is commoditizing. Trading intelligence — forecasting + optimization — is the differentiator.